## Slide 1
Architecture Changes in Wireless Networks
Video 2.3
The Evolution of Cellular and Wireless Networks

## Slide 2
Basic Architecture
PSTN
User
Equipment
(UE)
Radio
Access
Network
(RAN)
Public Switched Telephone Network
Core
Network
(CN)

## Slide 3
Air Interface
Layer 3
Network
Layer 2
Data
Layer 1
Physical
Open Systems
Interconnection Layer
NAS: Non-Access Stratum
RRC: Radio Resource Control
SDAP: Service Data Adaptation Protocol
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Control
MAC: Medium Access Control
PHY: Physical

## Slide 4
Air Interface
Layer 3
Network
Layer 2
Data
Layer 1
Physical
Open Systems
Interconnection Layer
NAS: Non-Access Stratum
RRC: Radio Resource Control
SDAP: Service Data Adaptation Protocol
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Control
MAC: Medium Access Control
PHY: Physical
User Plane: Exchanges data between Core Network and UE; also called Data Plane.
Control Plane: Sets up and tears down connections, responsible for routing.

## Slide 5
Basic Architecture
PSTN
User
Equipment
(UE)
Radio
Access
Network
(RAN)
Public Switched Telephone Network
Core
Network
(CN)

## Slide 6
2G Architecture
PSTN
User
Equipment
(UE)
Radio
Access Network
(RAN)
Public Switched Telephone Network
Core
Network
(CN)
MSC
BSC
BTS
BTS
BSS
BTS: Base Transceiver Station
BSC: Base Station Controller
BSS: Base Station Subsystem
MSC: Mobile Switching Center

## Slide 7
2.5G Architecture
PSTN
User
Equipment
(UE)
Radio
Access Network
(RAN)
Public Switched Telephone Network
Core
Network
(CN)
MSC
BSC
BTS
BTS
BSS
IP
Network
SGSN
GGSN
SGSN: Serving GPRS Support Node
GGSN: Gateway GPRS Support Node
General Packet Radio Service
(GPRS)

## Slide 8
3G Architecture
PSTN
User
Equipment
(UE)
Radio
Access Network
(RAN)
Public Switched Telephone Network
Core
Network
(CN)
MSC
RNC
Node B
Node B
RNS
IP
Network
SGSN
GGSN
RNC: Radio Network Controller
RNS: Radio Network Service

## Slide 9
4G Architecture
User
Equipment
(UE)
Radio
Access Network
(RAN)
Core
Network
(CN)
eNodeB
eNodeB
EPC
IP
Network
PGW
MME
SGW
MME: Mobility Management Entity
PGW: Packet Gateway
SGW: Serving Gateway
EPC: Evolved Packet Core

## Slide 10
5G NSA Architecture
User
Equipment
(UE)
Radio
Access Network
(RAN)
Core
Network
(CN)
eNodeB
eNodeB
EPC
IP
Network
PGW
MME
SGW
gNodeB
MME: Mobility Management Entity
PGW: Packet Gateway
SGW: Serving Gateway
EPC: Evolved Packet Core

## Slide 11
5G NR Architecture
User
Equipment
(UE)
Radio
Access Network
(RAN)
Core
Network
(CN)
gNodeB
gNodeB
IP
Network
5G Core
DU
gNodeB
DU
DU
CU
NEF
NRF
PCF
UDM
AUSF
AMF
SMF
NSSF
DU: Distributed Unit
CU: Centralized Unit
NRF: Network Repository Function
UDM: Unified Data Management
SMF: Session Management Function
NSSF: Network Slice Selection Function
NEF: Network Exposure Function
PCF: Policy Control Function
AUSF: Authentication Server Function
AMF: Access and Mobility Function

## Slide 12
KEY TAKEAWAYS
2G and 3G Driven by Voice Prioritization
2G and 3G networks were driven primarily by voice communication.
4G Driven by Data Prioritization
Full packet data network evolution occurred with the deployment of 4G.
4G and 5G Relationship
5G will not fully replace 4G for several years and will utilize 4G EPC as part of 5G NSA architecture.
01
02
03

## Slide 13
Potential Vulnerabilities and Risks
Next Video