## Slide 1
5G Non-standalone Networks
Video 3.3
Fundamentals of 5G Wireless Networks

## Slide 2
5G NSA Architecture
User
Equipment
(UE)
Radio
Access Network
(RAN)
Core
Network
(CN)
eNodeB
eNodeB
EPC
IP
Network
PGW
MME
SGW
gNodeB
MME: Mobility Management Entity
PGW: Packet Gateway
SGW: Serving Gateway
EPC: Evolved Packet Core

## Slide 3
5G NSA Architecture
User
Equipment
(UE)
Radio
Access Network
(RAN)
Core
Network
(CN)
eNodeB
eNodeB
EPC
PGW
MME
SGW
gNodeB
MME: Mobility Management Entity
PGW: Packet Gateway
SGW: Serving Gateway
EPC: Evolved Packet Core
5G
UE
4G LTE Network
5G RAN
Control Plane
User Plane

## Slide 4: Key Highlights
Enter your subhead line here
User Equipment Attaches to 4G LTE, signals dual connectivity, and connects to 5G bearer for user traffic.
5G gNodeB Secondary node for dual connectivity, provides radio resources for data.
4G LTE eNodeB Provides authentication for 5G and transfers data delivery to 5G gNodeB.
Evolved Packet Core Authorizes the UE for dual connectivity to 5G and supports switching to 5G.
5G
UE

## Slide 5
KEY TAKEAWAYS
5G NSA Provides Faster Deployment
Mobile Network Operators can deploy 5G faster and support 5G UEs.
5G NSA Utilizes 4G LTE Infrastructure
5G leverages 4G EPC for set-up and control on 5G gNodeB.
UE Must Be Capable of 5G Radio
Only User Equipment capable of supporting 5G radiofrequencies are support in 5G NSA.
01
02
03

## Slide 6
5G Standalone Networks
Next Video