## Slide 1
Subscriber Privacy
Video 6.2
Core Principles for Network Security

## Slide 2: Subscriber Privacy
Notes: Something that needs to grab the viewers attention!!

## Slide 3: 76%
of global consumers rated personal privacy as a top issue.
Notes: Something that needs to grab the viewers attention!!

## Slide 4
Represents relationship between the subscriber and mobile network operator.
Used to confirm user’s identity, location, and to eavesdrop on calls and data.
Sent unencrypted in 2G, 3G, and 4G networks when device first connects.
IMSI Catchers were able to intercept and perform Man-in-the-Middle attacks.
International Mobile Subscriber Identity (IMSI)
Notes: Picture downloaded from Pixabay: https://pixabay.com/vectors/network-iot-internet-of-things-782707/

## Slide 5
International Mobile Subscriber Identity (IMSI)
Represents relationship between the subscriber and mobile network operator.
Used to confirm user’s identity, location, and to eavesdrop on calls and data.
Sent unencrypted in 2G, 3G, and 4G networks when device first connects.
IMSI Catchers were able to intercept and perform Man-in-the-Middle attacks.
Notes: Picture downloaded from Pixabay: https://pixabay.com/vectors/network-iot-internet-of-things-782707/

## Slide 6
Subscription Permanent Identifier (SUPI):
  Similar to IMSI in 5G phones.
  Globally unique to each subscriber.
  Defined in 3GPP TS 23.501.
  Provisioned in the Universal SIM (USIM) module and 5G Core UDM/UDR.
Format:
  MCC/MNC/MSIN.
  3 digits for Mobile Country Code.
  2 or 3 digits for Mobile Network Code.
  9 or 10 digits for Mobile Subscriber Identification Numbers.
5G – SUPI and SUCI

## Slide 7
Subscription Concealed Identifier:
  Encrypted version of the SUPI sent over-the-air.
  Elliptic Curve Integrated Encryption Scheme (ECIES) used via Home Network (HN) public key stored in USIM during provisioning.
  SUCI is sent over-the-area for authentication and authorized access.
5G – SUPI and SUCI

## Slide 8
5G Identity Process
gNodeB
UDM
AUSF
AMF
Core
UE
UE encrypted SUPI as SUCI
Registration Request (SUCI)
UDM decrypts
SUCI to get SUPI
Authentication Response (SUPI)
AMF generates GUTI for mapping of SUPI
Registration Accept (GUTI)
Authentication Request (SUCI)
RAN

## Slide 9: Advantages
5G SIM Encryption
Ownership and Control Security managed end-to-end in network.
Higher Level Security Tamper-resistant SIM cards.
Seamlessness Faster and more secure access to network.
Interoperability 5G SIMs work in multiple implementations.

## Slide 10
Key Takeaways
Subscriber Privacy is a Major Issue
US and Europe closely monitoring.
Legacy Wireless Networks at Risk
IMSI exposed in 2G, 3G, and 4G.
5G Utilizes SUPI and SUCI
MSIN is concealed.
01
02
03

## Slide 11
Secure Communications
Next Video