## Slide 1
Centralized Identity Management
Video 6.4
Core Principles for Network Security

## Slide 2: Centralized Identity Management
Authentication and authorization of User Equipment, subscribers, and applications or services
Notes: Something that needs to grab the viewers attention!!

## Slide 3
5G SA Architecture
User
Equipment
(UE)
Radio
Access Network
(RAN)
Core Network (CN)
gNodeB
IP
Network
5G Core
DU
CU
NEF
NRF
PCF
UDM
AUSF
AMF
SMF
NSSF
MEC: Multi-access Edge Computing
5G
UE
MEC

## Slide 4
5G Identity Management
5G Core
Service Based Architecture
5G
UE
gNB DU
gNB CU
ARPF
SEPP
UDM
AUSF
AMF
SEAF
SIDF
AMF: Access Management Function
SEAF: Security Anchor Function
SEPP: Securing Protection Proxy
AUSF: Authentication Server Function
SIDF: Subscription Identifier De-concealing Function
UDM: Unified Data Management
ARPF: Authentication Credential Repository and Processing Function
UDR

## Slide 5
Subscription-Centric Identity (Access based on “network”)
  3GPP defined.
  Can support user identity to external services.
  Extension of 3GPP services to non-3GPP devices.
  Can provide security in the provided identity.
Centralized Identity Models

## Slide 6
User-Centric Identity (Access based on “user”)
  Exists on top of existing subscription authentication.
  Supports authentication and interactions with authentication system.
  Doesn’t replace subscription credentials.
  Supports service and layer identity of the user.
Centralized Identity Models
User
User Identity 1
User Identity 2
User Identity n
User Identifier A
User Identifier B
User Identifier C
Attribute a
Attribute b
Attribute X
User Identifier X
Attribute c

## Slide 7: Use Cases
User-Centric Model
UE Device Sharing
One UE (e.g., tablet) with access to 3GPP network.
Multiple users.
Industrial IoT
Several IoT devices communicating to local network.
Access via non-3GPP device.
Network Slice Authentication
Authorized for network.
Subscription validation allows slice assignment.

## Slide 8
Key Takeaways
5G Offers Robust CIM
Defined and standardized
SBA Supports Authentication
UDM is key network function
Subscription and User Models
Increases leverage and collaboration
01
02
03

## Slide 9
RAN and Core Network Security
Next Video