## Slide 1
Protocol Vulnerabilities
Video 7.2
Protocol Vulnerabilities

## Slide 2
Protocols
Layer 3
Network
Layer 2
Data
Layer 1
Physical
Open Systems
Interconnection Layer
NAS: Non-Access Stratum
RRC: Radio Resource Control
SDAP: Service Data Adaptation Protocol
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Control
MAC: Medium Access Control
PHY: Physical

## Slide 3
Protocols
Layer 3
Network
Layer 2
Data
Layer 1
Physical
Open Systems
Interconnection Layer
NAS: Non-Access Stratum
RRC: Radio Resource Control
SDAP: Service Data Adaptation Protocol
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Control
MAC: Medium Access Control
PHY: Physical
User Plane: Exchanges data between Core Network and UE; also called Data Plane.
Control Plane: Sets up and tears down connections, responsible for routing.

## Slide 4: Protocol Vulnerabilities
5G Networks
Function Security standards recommended or required but not implemented.
Scan Found Vulnerabilities found during function, configuration, or port scans.
Fuzz Discovered Finding defects and abnormal behavior through random and unexpected inputs.
Penetration Approach using holistic knowledge of network, tools, and gaps.

## Slide 5: Protocol Vulnerabilities
5G Networks
Function Security standards recommended or required but not implemented.
Examples:
Optional NAS and RRC confidentiality.
Optional UP integrity in some cases.
Mitigation:
Choose highest level ciphering algorithms.
  128-NEA-3 for confidentiality.
  128-NIA-3 for integrity.
If not possible, send only non-identity related information.

## Slide 6: Protocol Vulnerabilities
5G Networks
Scan Found Vulnerabilities found during function, configuration, or port scans.
Examples:
RAN network function configurations.
5G Core network function ports.
Mitigation:
Use commercial products to scan for vulnerabilities.
Take action to mitigate.

## Slide 7: Protocol Vulnerabilities
5G Networks
Fuzz Discovered Finding defects and abnormal behavior through random and unexpected inputs.
Examples:
Malformed packets through a rogue base station.
IoT manipulation.
Mitigation:
Test networks against vulnerability.
Use scale, load, and performance testing.

## Slide 8: Protocol Vulnerabilities
5G Networks
Penetration Approach using holistic knowledge of network, tools, and gaps.
Examples:
SUPI transmitted without encryption via UE manipulation.
“Bid down” to less secure 4G LTE.
Mitigation:
Hire experts to conduct “white hat” testing.
Train and utilize Security Operations team.

## Slide 9
Key Takeaways
Protocol Ciphering Can Be Optional
Should try to avoid these, if possible.
Vulnerabilities Exist
Function, Scan, Fuzz, and Penetration.
Mitigation is Possible
Acknowledge and act.
01
02
03

## Slide 10
AKA Attacks
Next Video