## Slide 1
Section 7
AKA Attacks
SECTION 7.3

## Slide 2
AKA Attacks
Video 7.3
Vulnerability, Threat Vectors, and Mitigation

## Slide 3
What is AKA?
AKA
Authentication & Key Agreement
Symmetric Cryptography
Where encryption and decryption keys the same
5G Authentication
Security protocol that is challenge-based using…
5G-AKA
EAP-AKA’ (Prime)
EAP-TLS

## Slide 4
Authentication Framework
UE
AMF
SEAF
N3IWF
AUSF
UDM
ARPF
SIDF
3GPP Network
Non-3GPP Network
WLAN
gNB
IPsec
UE: User Equipment
gNB: G-NodeB Base Station
WLAN: Wireless LAN
AMF: Access and Mobility Management Function
SEAF: Security Anchor Function
N3IWF: Non-3GPP Internetworking Function
AUSF: Authentication Server Function
UDM: Unified Data Management
ARPF: Authentication Credential Repository and Processing Function
SIDF: Subscription Identifier De-concealing Function
IPSec: IP Security protocol

## Slide 5
5G-AKA Authentication
gNodeB
UDM
AUSF
AMF
Core
UE
UE encrypted SUPI as SUCI
Authentication Request (SUCI)
UDM/ARPF/SIDF decrypts SUCI to get SUPI and selects authentication method
Authentication Response
Authentication Request (SUCI)
RAN
SEAF
ARPF
SIDF
Authentication Request (SUCI)
Hash computation
Authentication Response
Authentication Request

## Slide 6
5G Authentication Process
gNodeB
UDM
AUSF
AMF
Core
UE
Check Authentication
Authentication Response
RAN
SEAF
ARPF
SIDF
Check Response
Authentication Response
Check Response
Authentication Success

## Slide 7
EAP-AKA’
  Like 5G-AKA.
  EAP messages in NAS between UE, SEAF, and AUSF.
  SEAF is just a pass-through – no authentication work.
  EMSK use of first 256 bits.
EAP-TLS
  Limited use for private networks and IoT.
  SEAF is pass-through.
  Mutual authentication via a certificate or pre-shared key.
  EMSK use of first 256 bits.
Other 5G Authentication

## Slide 8
IMSI / SUPI interception.
  Can lead to spoofing, denial-of-service attacks, and man-in-the-middle attacks.
Attach and registration procedures.
  Unencrypted information sent to gNodeB.
  Can “bid down” UE to less-secure wireless generation.
5G Non-Standalone uses 4G LTE infrastructure.
  4G LTE protocols are less secure.
SUCI may have null encryption method (aka, no encryption).
  Encryption is optional.
  Unencrypted for emergency services.
AKA Attack Vectors

## Slide 9
Key Takeaways
5G Provides Authentication Security
5G-AKA, EAP-AKA’, EAP-TLS.
Vulnerabilities Still Exist
AKA attacks still possible but harder.
SUCI Concealment is Optional
Strongly recommended.
01
02
03

## Slide 10
Disclosure of Subscriber Unique Identifier
Next Video